## Slide 1
Lavakumar Veludandi -108019275556
Gursimran Singh -108019265806
Herol Lawrence Dsouza -108019265602
Naresh Kothavandla -108019265799
Design Optimization
Optimization of Four Bar Mechanism’s linkages for custom paths

## Slide 2: Contents
Introduction
Applications
Design variables
Objective function
Differential Evolution
Topology Optimization
Results
Conclusion

## Slide 3: Introduction
How does a four bar mechanism work?
Path generation using precision points.
Drawbacks of analytical methods.
Why optimization methods?
Goals …!!!
  Determine the length of the links
  Position of fixed points
  To generate the desired path
Ternary link
A
Crank
Coupler
Rocker
Frame

## Slide 4: Applications
Pumpjack
(rotary to reciprocating)
Bicycle Pedaling
(reciprocal to rotary)
Knee joint
(restricted motion)
Parrot fish jaw
(force multiplication)
Image Source:
https://hackaday.com/2017/03/29/
marvelous-mechanisms-the-ubiquitous-four-bar-linkage/

## Slide 5: Design variables
Nine design variables
r1, r2, r3, r4, r5, β, xA,yA and α.
Where,
r1, r2, r3 & r4 = lengths of the link.
r5 & β = determines the path.
(xA,yA) & α = position and orientation
of the fixed link.
Four optimization variables xA, yA, r3 & β

## Slide 6: Objective function
Objective function:
= + ( s + l > p + q ) × + ( ≠ s ) ×
where, & are penalty values
Constraint-1:
“Grashof condition: (s + l < p + q)”
s = shortest link, l = longest link, p, q = remaining links
Constraint-2:
“r2 must be the shortest length of the mechanism”

## Slide 7: Objective function
Constraint-3: Circular Proximity Function (CPF)
    CPF -> Error function for optimisation
    Analytical function for best fitting circle
CPF= Ri2–2)2
Where,
            Ri2 = (XD–Xc )2 + (YD–Yc)2
            2 is mean of Ri2
    The dimensionless CPF
    CPF= 2
(XD , YD)
(Xc , Yc)

## Slide 8: Objective function
Traced points at C
CPF
Optimized circle at D
Precision points at M and
Set of circles for precision points at C.
Computes the point D and the length of r4,r1, inclined angle alpha
= Rmax
= Rmin

## Slide 9: Optimization Process
Y
X
y
A
B
C
r2
r3
r5
M
xA
yA
β
1
D1
D2
D3
D4
D5
2
3
4
5
α
r4
r1
After CPF
D
Desired Path

## Slide 10: Differential Evolution
Stochastic population based technique.
Each solution undergoes mutation followed by recombination.
Greedy selection is performed between target and trial vectors.
Target
Vector
Mutation
Trial
Vector
Donor
Vector
Recombination
Objective function
Population size
Lower & Upper bounds
Number of iterations
Crossover probability
Scaling Factor
User inputs

## Slide 11: Differential Evolution
A matrix of M of size (NP,m) is generated based randomly
M = repmat(lb,Np,1).*rand(Np,D) + repmat((ub-lb),Np,1).*rand(Np,D)
Each entry of M is within the prescribed bounds by the user
V1,1 | V1,2 | V1,3 | V1,4
V2,1 | V2,2 | V2,3 | V2,4
V3,1 | V3,2 | V3,3 | V3,4
V4,1 | V4,2 | V4,3 | V4,4
VNP,1 | VNP,2 | VNP,3 | VNP,4
V1,m
V2,m
V3,m
V4,m
VNP,m
NP : Population Size
V : Target Vector
D : Length of target vector
lb : Lower Bound
ub : Upper Bound
Target Vector
Selected Xr1
Selected Xr2
Selected Xr3

## Slide 12: Mutation
Donor Vector (V) is created as:
Target vector is not involved in mutation
Total 4 vectors are involved in mutation of target vector, hence
Np is the population size
V = Xr1 + F (Xr2 – Xr3)
F Scaling factor between 0 and 2
Xr1,r2,r3 Random solutions
Np ≥ 4
Differential Evolution

## Slide 13: Recombination: Binomial (uniform) crossover
Performed to increase the diversity
Example:
Differential Evolution
Conditions :
Target Vector
Donor Vector
pc crossover probability
δ randomly selected variable location
r random number between 0 and 1
uj jth variable of trial vector
vj jth variable of donor vector
xj jth variable of target vector
x1
v2
v3
x4
v5
r > pc
r > pc
r ≤ pc
j ≠ δ
j ≠ δ
j = δ
r > pc
r ≤ pc
j ≠ δ
j ≠ δ
r > pc
r > pc
Trial Vector

## Slide 14: Bounding offspring
Differential Evolution
lb
ub
xnew
Xnew is within bounds
No bounding required
lb
ub
xnew
Xnew violates upper bound
Shift xnew to upper bound
lb
ub
xnew
Xnew violates lower bound
Shift xnew to lower bound
lb
ub
xnew
lb
ub
xnew

## Slide 15: Greedy Selection
D1
D2
D3
D4
D5
Differential Evolution
x1
x2
x3
x4
x5
Target Vector
Trial Vector
Objective Function
Objective Function
λ
μ
Finally: if:
λ > μ Select Trial Vector
λ < μ Select Target Vector

## Slide 16
Design Variables
X
Process Flowchart
Objective Function
CPF
Convergence
Output
yes
Differential Evolution
no

## Slide 17
Variable | Optimized Values
r1 | 1.85
r2 | 1.69
r3 | 2
r4 | 1.83
r5 | 4.45
β | 0.16
xA | 1
yA | 4.95
α | -0.27
Units : Lengths : meters
Angles : radians
Results Problem 1:
Total number of precision points: 25

## Slide 18
Variable | Optimized Values
r1 | 6.27
r2 | 1.72
r3 | 2.37
r4 | 5.62
r5 | 2.89
β | -0.04
xA | 0
yA | 4.5
α | 2.76
Units : Lengths : meters
Angles : radians
Results Problem 2:
Total number of precision points: 90

## Slide 19: Animation
PROBLEM-1
PROBLEM-2

## Slide 20: Topology optimization: Problem 1 – Ternary Link
Von-Mises stresses before optimization
Shape of the link as a result of topology optimization
Material : Steel
Young’s modulus: 210 GPA

## Slide 21: Topology optimization: Problem 1 – Ternary Link
Final shape of the link built based on
topology optimization
Von-Mises stresses of final design of the link

## Slide 22
Topology optimization: Problem 2 – Ternary Link
Von-Mises stresses before optimization
Shape of the link as a result of topology optimization
Material : Steel
Young’s modulus: 210 GPA

## Slide 23
Topology optimization: Problem 2 – Ternary Link
Final shape of the link built basing on
topology optimization
Von-Mises stresses of final design of the link

## Slide 24: Conclusions
Optimal synthesis of four-bar path generation of linkages.
Design Variables reduced from 9 to 4 using CPF.
50% volume reduction of the Ternary Link using TO in ABAQUS.
Applications: Milling machines.
Future Scope: Implementation using Neural Networks.
          Pros: 1) Huge dataset of precision points.
              2) Increased precision of traced path.

## Slide 25: References
Sahand Hadizadeh Kafash , Ali Nahvi, Optimal synthesis of four-bar path generator linkages using Circular Proximity Function, 2017.
A.J. Sommese , Complete solution of the nine-point path synthesis problem for four-bar linkages, J. Mech. Des. 114 (1992) 153.
G.P. Roston , R.H. Sturges , Genetic algorithm synthesis of four-bar mechanisms, Artif. Intell. Eng. Des. Anal. Manuf. 10 (1996) 371–390.
S.H. Kafash , A. Nahvi , Optimal synthesis of four-bar motion generator linkages using circular proximity function, Proc. Inst. Mech. Eng. Part C (2017) 892–908.
S.B. Matekar , G.R. Gogate , Optimum synthesis of path generating four-bar mechanisms using differential evolution and a modified error function, Mech. Mach. Theory 52 (2012) 158–179.

## Slide 26
Thank You for your kind attention…